SToGS – Simulation Toolkit fOr Gamma-ray Spectroscopy
User's guide

last modification 02/2021

Contributors

I. Companis, C.Ducoin, B. Rebeiro, O.Stézowski

# Introduction

The goal of the SToGS simulation package, based on GEANT4, is to provide an environment in which one can:

- design and study response functions of new detectors
- prepare experiments by providing realistic simulations and analysis
- provide and improve physics generators

The package inherits from the PARIS GEANT4 package. To fulfill the goals, SToGS has been developed to be usable under Geant4.10 (or more) using Multi-threading[1]. As the PARIS package, it is configurable using a general ascii file in order to select the 4 main GEANT4 ingredients:
[1] https://twiki.cern.ch/twiki/bin/view/GEANT4/QuickMigrationGuideForGEANT4V10

- the physics generator
- the physics list
- the geometry under study
- the way the physics is extracted out (User’s actions) of GEANT4
(For an introduction on GEANT4, see lectures (EIPS School) given @ Lyon in 2013, 2014 and 2018)

Several executables are provided to fulfill the different goals:

- SToGS_ImportGeo is used to convert geometries produced by other tools
- SToGS_DetectorBuilder helps you to create the setup you would like to work with
- SToGS_Source is used to run simulations with 'simple' sources, 'simple' in the sense that the primary simulated events are completely independent from tracking in the setup
- SToGS_Beam (to come) for 'real' experiments involving beams and reactions in GEANT4
Concerning the physics generator, users are encouraged to use the GPS (General Particle Source) Primary Generator[2] coming with the GEANT4 package. It allows to model simple and complex sources (random events from functions/distributions) using GEANT4 macros. An other generator EGPS (E for External) has been developed within the SToGS package. It allows to read primaries (in particular ROOT/Trees) from external files on an event by event basis. In the section Physics Generators details are given about the possibilities and how to configure the different generators.
[2] http://geant4-userdoc.web.cern.ch/geant4-userdoc/UsersGuides/ForApplicationDeveloper/fo/BookForApplicationDevelopers.pdf
As well, the configuration file allows to select the various physics lists provided by GEANT4. In case specifics are going to be developed, they are detailed in the section Physics lists.

Concerning geometries, the idea is to provide as much as possible geometries that can be imported/exported from/to different frameworks, including analysis frameworks. For that purpose, the GDML format[3] has been adopted as core of the system. Within SToGS, the concept of Detector Factory has been introduced. It provides containers of standard detectors (arrays) that can be assembled through a simple ascii file to form complex setups. Details concerning this part are given is the Geometries section.
[3] http://lcgapp.cern.ch/project/simu/framework/GDML/doc/GDMLmanual.pdf
The way the physics is extracted from GEANT4 is done through Action Managers. The different managers available are detailed in the corresponding section.
# Installation
Pre requirements:
C++ (at least cxx11)
git
cmake
a version of GEANT4 installed with the GDML module compiled

The SToGS package is hosted on a gitlab server at the following address:
https://gitlab.in2p3.fr/IPNL_GAMMA/stogs.git

As subversion (svn), mercurial (hg), git is adapted to software developments since it allows several developers to work on the same code and it keeps track of all evolutions of the code. A good documentation concerning git can be found here:
http://git-scm.com/book/fr or http://git-scm.com/book/en

Note that git manipulations are required only if you would like to be contributor of a git based package. To download the SToGS package, you should have the git command installed on your PC (by default in most of the standard linux distributions) or use the Download ZIP button on the github web pages. To get the package from github, from a terminal, you should type the following commands:

git clone https://gitlab.in2p3.fr/IPNL_GAMMA/stogs.git stogs

Cloning into 'SToGS'...
remote: Reusing existing pack: 130, done.
remote: Counting objects: 108, done.
remote: Compressing objects: 100% (107/107), done.
remote: Total 238 (delta 62), reused 0 (delta 0)
Receiving objects: 100% (238/238), 172.05 KiB | 0 bytes/s, done.
Resolving deltas: 100% (153/153), done.
Checking connectivity... done

cd stogs
ls

CMakeLists.txt README.md SToGS_Source.cc setup/ G4Macros SToGS_DetectorBuilder.cc csrc/

Note: The list of files given by the ls command is likely to change over time and is given there only as an indication of what could be expected.

Once in the SToGS directory, it is recommended, in order to configure/compile the package, to create one directory per version of GEANT4 you would like to play with. The following supposes that you have installed Geant4.10.0.

mkdir geant4.10.XX-release
cd geant4.10.XX-release
cmake -DGeant4_DIR=/where/geant4/has/been/built ../
make
ls
CMakeCache.txt Makefile SToGS_Source CMakeFiles SToGS_DetectorBuilder cmake_install.cmake

If the configuration[cmake]/compilation[make] is ok, you should have the SToGS executables in the directory. To run them, see the next sections.
# Running a SToGS application
## Running SToGS_DetectorBuilder

Figure: AGATA Geometry displayed using StoGS_DetectorBuilder (Qt based GEANT4 version)

This application allows the user to build his setup and save it to be run in SToGS_Source and/or SToGS_Beam[4]. The goal is mainly to build the setup [geometry, active volumes, detector mapping] and check for overlapping volumes by running some tests and using graphical tools like Qt or HepRep.
[4] Not yet available
In the SToGS directory, you can run the DetectorBuilder using the command:

./geant4.10.XX-release/SToGS_DetectorBuilder

The first time you run it, it fills automatically the factory with some standard detectors (this could take few minutes). Here is for instance a piece of the produced output.

[+..] Building Detector aChateau2Crystal_bare
[W] in SToGS::MaterialConsultant::FindOrBuildMaterial AIR replaced by SToGS_AIR
[W] in SToGS::MaterialConsultant::FindOrBuildMaterial BaF2 replaced by SToGS_BaF2
[+[SToGS::UserActionInitialization::GetCopClusterSD()]] Creating a CopCluster SD
[_[SToGS::UserActionInitialization::GetCopClusterSD()]] Creating a CopCluster SD
G4GDML: Writing 'DetectorFactory/Scintillators/aChateau2Crystal_bare.gdml'...
G4GDML: Writing definitions...
G4GDML: Writing materials...
G4GDML: Writing solids...
G4GDML: Writing structure...
G4GDML: Writing setup...
G4GDML: Writing surfaces...
G4GDML: Writing 'DetectorFactory/Scintillators/aChateau2Crystal_bare.gdml' done !
[..+] Building Detector aChateau2Crystal_bare

It tells that one module of 'le chateau de cristal' has been built in the factory Scintillators. Adding a detector in a factory means:
- creating a .gdml file that contains the full description of the geometry
- creating a .amap file that contains the detector in terms of attributes
  [colors, sensitivity, fields, etc ...]
- creating a .dmap file that provides a mapping of the detector mandatory for analysis

Once the different factories have been filled with their detectors, you can use them to build different setups or use them directly to run simulations with the other SToGS tools.

## Running SToGS_ImportGeo
With the SToGS_DetectorBuilder application you can build setups from the various detectors already in the factories. It might be useful to import in the SToGS framework geometries produced in other frameworks for instance CAD like gemoetries. The SToGS_ImportGeo application might be used to do such transformations. It is based on CADMesh and so far deal with .ply and .stl files. Here is the command to import a stl file into gdml, the left geometry being shown being the .stl as seen in meshlab the right one in Geant4/Qt

./geant4.10.XX-release/SToGS_ImportGeo -input add-ons_geo/stl/SideWallsATC180.stl -detname DetectorFactory/MyStore/SideWallsATC180

.stl in meshlab	Converted .stl in .gdml in Geant4/Qt

More about conversions of geometries in the Geometries section.
## Running SToGS_Source
To run this application one needs to fully define all the GEANT4 modules. They are selected using a configuration file, which is by default expected to be:

setup/SToGS_Source.conf

Here is a snapshot of such a file. An example is provided in the directory setup/SToGSDefault/.

# This is the default file used to configure the SToGS_Source program.
# It is read at the beginning of the program to select
#
# The UserActionInitialization (which deals without outputs and the generator [thread local objects])
#
actions: printout run;event;track;step
#actions: ascii setup/SToGS_ascii_actions.conf
#
# Detector geometry
#
setup: factory DetectorFactory/Generics/TwoShells
#setup: factory DetectorFactory/Scintillators/ParisPW_2
#
# The Physics list
#
physics: stogs_m general0;emstandard_opt0;
#physics: general0;emstandard_opt0;Optical;
#
# generator
#
generator: GPS G4Macros/GPS_Cs137.mac
#
# In case of MT, allows the user to specify the number of threads
#
nbthread: 2
#

The symbol # starts a comment and an input starts with a key word. There are several key words to customize the simulation.

If you want to use your own configuration file (let us call it MyConfig.conf) instead of SToGS_Source.conf, you should execute SToGS_Source with the following option:

./geant4.10.XX-release/SToGS_Source -c MyConfig.conf

You can also use the -b option (batch) to call a file containing a list of commands to be executed after StoGS_Source.

## Running SToGS_Beam
Not yet developped but foreseen ...
# Physics lists
To run a GEANT4 application, the user has to select the physics into the game : without it, particles go through the detector without any interactions.
In the configuration files of SToGS, the physics lists are added using such a line :

# The Physics list
#
physics: stogs_m general0;emstandard_opt0;
#

With this line two physics lists are added. The one in charge of the transport of particles (general0 : in G4 transport is considered as a physics process) and the standard electromagnetic list (emstandard, option 0) obviously in charge of the electromagnetics processes. It is to be noted for instance with such a line, hadronic processes are not included thus a neutron is not going to interact with the detector.
So far some of the standard G4 physics lists (see GEANT4 web site) are included into SToGS.
general
emstandard_opt0
emstandard_opt1
emstandard_opt2
emstandard_opt3
emlivermore
empenelope
SToGS_hadron
QGSP_BIC_HP
# Physics Generators
As for real experiments, the user should determine the initial condition which trigs a new event. In real experiment it could be a beam on a target or a source. In GEANT 4, this is done using Physics Generators. GEANT4 provides one, called GPS (General Particle Source) able to generate particles from probability distributions (functions and/or distributions). In SToGS this physics generator is selected using such a line, the second parameter is the GEANT4 macro which contains the instructions:
# generator
#
generator: GPS G4Macros/GPS_Cs137.mac
#
Here is the content of the GPS_Cs137.mac file (see G4macros sub-directory):
/gps/particle gamma
/gps/pos/type Point
/gps/pos/centre 0. 0. -10. cm
/gps/ang/type iso
/gps/ene/type Mono
/gps/energy 661.7 keV

It set a source producing one gamma-ray from one point at position (0,0,-10). The emission is isotropic, mono-energetic, the energy being 661.7 keV. Much more is possible, go and see the GEANT4 web site for more.
In SToGS another generator is provided. The goal is to be able to read, on an event by event basis, what has been produced by an external generator. This is why it is called EGPS (for External General Particle Source). To understand how it works, one needs to explain the way GEANT4 organize the primary particles in primary events. Here is a picture :

Figure: Primary Events, Vertexes and Particles

As it can be seen, a primary event is composed of a set of vertexes and for each vertex, particles are emitted. A vertex is defined by a position and a time : all particles attached to a given vertex are emitted from the same position and the same time. A particle is defined by its type (this is done through the PDG code), a direction, a polarisation and an energy. One can also attached or not the vertex number the particle comes from (VertexID).
In EGPS, all or part of the information to build a primary event is read from files event by event. Because some information may not be in the input files, defaults are defined and are used to init any vertexes or particles. Once initialized, the data are modified from what is read from the files accordingly to what the user wants to read. Once an event is built, it can go through filters (called bias). At this level one can for instance add some noises. Here is a picture to illustrate this :

Figure: EGPS, initialisation and different steps to enhance the input events

The built event is then fired into the detector and GEANT4 takes care of the propagation of the particles.
Another feature provided by EGPS is to be able to speed up the whole process using the multi-thread mechanism set in GEANT4 (version > 4.10). Considering reading files, there are then two possibilities :
- Or the same file is read and events are dispached to different threads to be treated.
- Or each thread read independant files.
Depending on the case then, the external source is shared or not. Here is a picture to illustrate the two cases depending of the situation.

Figure: Parallelisation using EGPS

In this picture, three parallel threads process events. For efficiency, it has been decided into SToGS to add another independant thread in charge of reading the files : this thread prepares batches of events which are then passed to other threads performing (sequentially) the tracking of the events.
Let us see now how to configure EGPS to read events stored in ROOT TTree/TChains. Of course, to do this, SToGS must know ROOT. In principle it is detected by cmake if it is installed on your computer. TTree/TChains are efficient and compact ways to store events, this is why efforts have been made to be able to deal with such external sources of events[5]. To select EGPS as a generator, do this :
[5] More kind of data format might be added in the future.
# generator
#
generator: EGPS G4Macros/EGPS_TChain_OnlyGamma.mac
#

As for GPS, EGPS is configured using the GEANT4 macro facilities. Here is the first command to be given in the .mac file:
# add an external source based on a ROOT/TChain. It becomes the current external source
# first parameter unique name of the source, second is intensity, third is batch size, forth is to set the sharing mode
/egps/esource/addtchain es0 1. 500 0
#

This command (/egps/esource/addtchain) creates a new source of external events called es0. The second parameter gives the intensity of this source. The third parameter set the number of events inside one batch while the last one declares whether or not the source is shared between the processing threads. If shared, be sure the name of the source is unique !
Because one can have different parallel processing, it is important to apply commands whatever the thread or to a particular one.
NOTE:
The number of processing threads is set using the parameter nbthread in the SToGS_Source configuration file, see the follwing or the section Running SToGS_Source.
# In case of MT, allows the user to specify the number of threads
#
nbthread: 3
#

The command
# threadID = -1 : following this, the command are called whatever the thread
#
/egps/threadID -1
#

let EGPS knows the following commands are to be applied whatever the thread. Once a new external TTree/TChains source has been created, the name of the TTree/TChains should be given with the following command:
# TChain definition - name of the chain to be read
/egps/tchain/name ExternalEvents

As explained, one can get from the TTree/TChains only some information. The selected data to be read are given with the following
# what is to be read from the external source
/egps/esource/branches Pr.E;Pr.PDG;Pr.VID;

In such a case the energy, type of the particles emitted are read as well as a vertex id. The full list of avaibable branches is given later on with the details of the TTree/TChains structure.
Defaults can be provided for vertexes and particles. Here are the commands for that :
# default values for one primary eevnt ... could be given for all threads but also overwritten per thread
# default for a primary particle PDG E DX DY DZ PX PY PZ
/egps/default/particle 22 0.6617 0. 1. 1. 0. 0. 0.
# default for vertex VertexID T X Y Z
/egps/default/vertex 0 0. 0. 0. 0.
/egps/default/vertex 1 0. 0. 0. -10.
/egps/default/vertex 2 0. 0. 0. -20.

GEANT4 units are expected i.e. MeV for energies, mm for positions, ns for times. The number of vertexes can be different from one event to the other one. In case defaults have been set for a too short list, the list is expanded using the very last vertex defined. In SToGs one default vertex (vertex 0) is always defined (0 for time and position) and its values can of course be modified.
The last mandatory command to be applied is to provide the list of files to be read. For that it might be convenient to use one of the feature of the GEANT4 commands, the possibility to define aliases. In the following it is done to set the path where to read the files and a pattern for thoses files.
# Set here the path to the file as alias, convenient for changes
#
/control/alias path_to_input "/path/to/the/data"
/control/alias base_name_root_file "MyEvents"
#
/egps/threadID 0
/egps/esource/addfile {path_to_input}{base_name_root_file}0.root

# thread 1
/egps/threadID 1
/egps/esource/addfile {path_to_input}{base_name_root_file}1_0.root
/egps/default/vertex 1 0. 0. 0. 10.

# thread 2
/egps/threadID 2
/egps/esource/addfile {path_to_input}{base_name_root_file}2.root

# back to thread #1
/egps/threadID 1
/egps/esource/addfile {path_to_input}{base_name_root_file}1_1.root

The command (/egps/esource/addfile) adds files to the input list. Files are then here of the form :
/path/to/the/data/MyEventsXX.root

In this particular case, there is not sharing of the input data and the three threads process independant data : using the command /egps/threadID 2 tells the system the following commands are to be called only for the particular thread #2. One can see also defaults for vertex#1 have been modified but only for thread #1.
Here is the part defining the files to read in case the sources is shared:
# add an external source based on a ROOT/TChain. It becomes the current external source
# first parameter unique name of the source, second is intensity, third is batch size, forth is to set the sharing mode
/egps/esource/addtchain es0 1. 500 1
#
...
/egps/threadID -1
...
/control/alias path_to_input "/path/to/the/data"
/control/alias base_name_root_file "MyEvents"
#
/egps/esource/addfile {path_to_input}{base_name_root_file}0.root
/egps/esource/addfile {path_to_input}{base_name_root_file}1_0.root
/egps/esource/addfile {path_to_input}{base_name_root_file}1_1.root
/egps/esource/addfile {path_to_input}{base_name_root_file}2.root

As it can be seen from the previous paragraphs, EGPS allows to deal with different situations. In order to go deeper into details, one should see first what is the structure expected in the input files. Here is a snapshot (ROOT TTree/TChains) for a very simple case :

The Tree contains 100000000 entries and for each entry only the energy of the particle is given. The name of the Tree is ExternalEvents. The number of particle is one or two (see histogram Pr.nb) : in fact the tree contains an equal number of events coming from a Cs137 source (one gamma 0.662 MeV) and from a Co60 source (two gamma in coincidence, energies are 1.1732 and 1.3325 MeV). Obviously there is no information about the vertex from which those particles come. Only one can be defined and should be set through the EGPS commands. As well the other parameters for the particles emitted should be set. Here it is done :
# default values for one primary eevnt ... could be given for all threads but also overwritten per thread
# default for a primary particle PDG E DX DY DZ PX PY PZ
/egps/default/particle 22 0. 0. 0. 1. 0. 0. 0.
# default for vertex VertexID T X Y Z
/egps/default/vertex 0 0. 0. 0. -10.

Using this, the type of any particle emitted is set to PDG=22 (gamma-ray). The gamma-rays, unpolarized, are emitted in the z direction. The vertex to emit them is moved by -10 mm on the z axis.
# TChain definition - name of the chain to be read
/egps/tchain/name ExternalEvents
/egps/esource/branches Pr.E;

The command (/egps/esource/branches Pr.E;) set what is to be read event by event from the files.
One may want to set the vertex id from where particles are emitted. In the previous case the gamma-ray from the Cs137 might be at one position while the ones from Co60 at another one. Here is the tree structure showing such a case and at the same time the type of the emitted particle is also given in the Tree using the PDG code.
One can see that three type of particles are emitted (PDG=22, 2112 and 2212 respectively for gamma, neutron and proton). They may come from three different vertexes. As there is no information related to the vertex (position,time), this information has to be set as previously through some defaults.
# default values for one primary event ... could be given for all threads but also overwritten per thread
# default for a primary particle PDG E DX DY DZ PX PY PZ
/egps/default/particle 22 0. 0. 0. 1. 0. 0. 0.
# default for vertex VertexID T X Y Z
/egps/default/vertex 0 0. 0. 0. 0.
/egps/default/vertex 1 0. 0. 0. -10.
/egps/default/vertex 2 0. 0. 0. -20.
#
/egps/esource/branches Pr.E;Pr.PDG;Pr.VID;

The ROOT/Tree may also have the full definition of the vertexes for any event. This is of course for complex situations where the vertexes can be anywhere any time. Here is such a stucture :

Of course, since the verterxes are given event by event, the number of vertexes has to be there (Pr.nbv). In the example, only the positions (VX,VY,VZ) of the vertexes are given, thus the time information has to be given through the EGPS commands, otherwise it would have been one branch called Pr.VT.
# default values for one primary event ... could be given for all threads but also overwritten per thread
# default for a primary particle PDG E DX DY DZ PX PY PZ
/egps/default/particle 22 0. 0. 0. 1. 0. 0. 0.
# default for vertex VertexID T X Y Z
/egps/default/vertex 0 0. 0. 0. 0.
/egps/default/vertex 1 10. 0. 0. 0.
/egps/default/vertex 2 5. 0. 0. 0.
# ... add as many vertexes required ...
#
/egps/esource/branches Pr.E;Pr.PDG;Pr.VID;Pr.VX;Pr.VY;Pr.VZ

The last situation EGPS is able to handle is where a primary event is defined by a list of particles and each particle comes from a unique vertex. In this case one can of course have a tree structure as previously explained but it would be not efficient because we will have more information in the Tree that requires (the Pr.nb leaf equal to Pr.nbv, the Pr.VID useless). Here is the structure that can be defined for a more efficient treatment:

# default values for one primary event ... could be given for all threads but also overwritten per thread
# default for a primary particle PDG E DX DY DZ PX PY PZ
/egps/default/particle 22 0. 0. 0. 1. 0. 0. 0.
#
/egps/esource/branches Pr.E;Pr.PDG;Pr.X;Pr.Y;Pr.Z;Pr.T

Of course, using the command /egps/esource/branches, we do have the possibility to precisely select waht branches are read from the tree so that the tree structure can have more. The additionnal branches are ignored during the reading of the tree. The name of the different branches (Pr.E, Pr.PDG, etc...) are fixed so far but an alias mechanism is going to be added in the future.

The last feature available in EGPS is the possibility to apply biases on the event produced. For instance one may change the time of emission etc ... TO BE DONE and WRITTEN.
# Geometries
## How to build an array from detectors stored in the factory ?
This part explains how to use the factory and the SToGS_DetectorBuilder in order to prepare the setup you would like to work with.
To to this, what is required is an ascii file which has the .dfb extension [standing for Detector Factory Builder]. There are several such files in the SToGS package, and one [default.dfb] is provided in the top directory. Copy it so that you can customize your own file:
cp default.dfb my.dfb

Here is an example of the content of such a file with the appropriate comments to know what is the effect of each line:
#
# First the world is defined.
# if it does not exist in the factory, a box with dim [1. 1. 1. m] given otherwise dim ignored
#
w DetectorFactory/Rooms/VR 1. 1. 1. m
#
# With this line, one can change the current global copy number.
# At loading time, the detector numbers
# are read from the factory and added to this offset.
# Allows to add many detectors with their own range of unique number
#
@ 0 ->
#
# This line add to the world a PARIS Cluster at position (0.,0.,25.) cm
#
+ DetectorFactory/Scintillators/CParisPW_2 0. 0. 25. cm
#
# end

If you have a GEANT4 installation using a geometry driver [like Qt in this exemple], you should get a window showing a view of a PARIS Cluster by running the following command[6]:
[6] It is mandatory to run the application from the top SToGS directory i.e. where is the file SToGS_DetectorBuilder.cc
./geant4.10.XX-release/SToGS_DetectorBuilder -dfb my.dfb

The left side of the window displays a tree description of the setup, which, in this example, is composed of a Virtual Room [VT] containing the 18 active volumes of the PARIS cluster. Each active volume is fully identified by the following type of code:
CParisPW_2:000:ParisPW_2:005:PW:1: [11]

This means that the active volume number 11 is inside the cluster number 000 [CparisPW_2:000], inside the phoswich number 005 [ParisPW_2:005] and belongs to the second stage of the phoswich [PW:1].

More complex setups can be built involving any kind of detector and any kind of translation – rotation. Here is another example with a PARIS cluster, an EXOGAM clover and an AGATA Triple cluster at different distances and angles, all pointing to the center:
#
w DetectorFactory/Rooms/VR 1. 1. 1. m
#
+ DetectorFactory/Scintillators/CParisPW_2 0. 0. 25. cm
+ DetectorFactory/SemiConductors/Ge/EXOCLOVER_A-AC 0. 0. 10. cm Ry 90 Rt
+ DetectorFactory/SemiConductors/Ge/ATC 0. 0. 15. cm Ry -90 Rt
#
# end

After the translation of given object, one can add any combination of rotations by simply giving the axe to turn around followed by the angle in degrees. The last string Rt tells SToGS to apply also the rotation to the given translation before placing the object in the world.
Note the symbol + at the beginning of the lines. In case you would like to add many times the same detector, you should use the * symbol. Here is a partial snapshot of the .dbf file used to build the full AGATA array. Note the block of snapshots starts with [ and ends with ].
[
* DetectorFactory/SemiConductors/Ge/ATC	+74.4705	+71.7883	-256.432	mm Rz +344.302 Ry +158.032 Rz +43.9494
* DetectorFactory/SemiConductors/Ge/ATC	-45.2621	+93.0094	-256.432	mm Rz +344.302 Ry +158.032 Rz +115.949
* DetectorFactory/SemiConductors/Ge/ATC	-102.444	-14.3054	-256.432	mm Rz +344.302 Ry +158.032 Rz +187.949
* DetectorFactory/SemiConductors/Ge/ATC	-18.0517	-101.851	-256.432	mm Rz +344.302 Ry +158.032 Rz +259.949
* DetectorFactory/SemiConductors/Ge/ATC	+91.2874	-48.6418	-256.432	mm Rz +344.302 Ry +158.032 Rz +331.949
]

In case you are using Qt to see geometries, you should have a window similar to this one for the setup comprising a PARIS cluster, an EXOGAM clover and an AGATA Triple cluster:

At this level, you should check if your setup is OK, i.e. whether or not some volumes are overlapping and if the mapping of the setup is suitable for your needs[7]. The first point can be done graphically of course. A GEANT4 test is also run when you execute StoGS_DetectorBuilder, and if the test is passed you should get in the running terminal the following sentences:
[7] Mapping is required to recover what is going on in the simulation at the analysis level.
GeomTest: no daughter volume extending outside mother detected.
GeomTest: no overlapping daughters detected.

On the left side, one can see the description of the whole array in terms of names and mapping. In principle passive volumes in SToGS have an ID equal to -1 and any active volume could be uniquely identified. For active volumes directly under the world, this is the number given under bracket [] and for those deeper in the tree structure, you should add the top ID number to the ID of the active volume. For instance, for AGATA, the green capsule would be identified by [24]+[1].
Once you are satisfied with the setup, you can save it in your GEANT4 session using the command:
DetectoryFactory/Save MySetup

The array can be retrieved in MyStore factory and used for other purpose, as explained in the next session.
## What is in the Factory and how to look for detectors from there ?
The first time the application SToGS_DetectorBuilder is run, the full DetectorFactory is completed i.e. some standard known detectors are built (from c++ code inside the SToGS package) giving for each detector the three files:
- .gdml file that contains the full description of the geometry
- .amap file that contains the detector in terms of attributes [colors, sensitivity, fields etc ...]
- .dmap file that provides a mapping of the detector mandatory for analysis

Depending on the version of SToGS you are running, the content can be different. All the detectors can be found in the DetectorFactory directory, and there are sub-containers to store for instance Semiconductors or Scintillators. Here is a snapshot giving the structure [03/2015]:
tree -d DetectorFactory/
DetectorFactory/
|-- Arrays
|   `-- Builders
|-- Generics
|   `-- Demos
|-- MyFactory
|   `-- Builders
|-- MyStore
|   `-- Builders
|-- Imports
|-- PlaneDetectors
|-- Rooms
|   `-- Builders
|-- Scintillators
|   `-- Builders
`-- SemiConductors
    `-- Ge
        `-- Builders

Here is also a detail of some factories:
DetectorFactory/SemiConductors/ / `-- Ge / |-- AGATA-ARed.amap / |-- AGATA-ARed.dmap / |-- AGATA-ARed.gdml / |-- AGATA-ARed_bare.amap / |-- AGATA-ARed_bare.dmap / |-- AGATA-ARed_bare.gdml / |-- AGATA-BGreen.amap / |-- AGATA-BGreen.dmap / |-- AGATA-BGreen.gdml / |-- AGATA-BGreen_bare.amap / |-- AGATA-BGreen_bare.dmap / |-- AGATA-BGreen_bare.gdml / |-- AGATA-CBlue.amap / |-- AGATA-CBlue.dmap / |-- AGATA-CBlue.gdml / |-- AGATA-CBlue_bare.amap / |-- AGATA-CBlue_bare.dmap / |-- AGATA-CBlue_bare.gdml / |-- ATC.amap / |-- ATC.dmap / |-- ATC.gdml / |-- ATC_bare.amap / |-- ATC_bare.dmap / |-- ATC_bare.gdml / |-- Builders / | |-- agata_capsule.geo / | |-- agata_cluster.geo / | |-- agata_euler.geo / | `-- empty.dfb / |-- EXOCLOVER_A-AC.amap / |-- EXOCLOVER_A-AC.dmap / |-- EXOCLOVER_A-AC.gdml / |-- EXOCLOVER_A-bare.amap / |-- EXOCLOVER_A-bare.dmap / `-- EXOCLOVER_A-bare.gdml	DetectorFactory/Scintillators/ / |-- Builders / | `-- empty.dfb / |-- CParisPW_2-bare.amap / |-- CParisPW_2-bare.dmap / |-- CParisPW_2-bare.gdml / |-- CParisPW_2.amap / |-- CParisPW_2.dmap / |-- CParisPW_2.gdml / |-- ParisPW_2-bare.amap / |-- ParisPW_2-bare.dmap / |-- ParisPW_2-bare.gdml / |-- ParisPW_2.amap / |-- ParisPW_2.dmap / |-- ParisPW_2.gdml / |-- ParisPW_3-bare.amap / |-- ParisPW_3-bare.dmap / |-- ParisPW_3-bare.gdml / |-- ParisPW_3.amap / |-- ParisPW_3.dmap / |-- ParisPW_3.gdml / |-- aChateau2Crystal.amap / |-- aChateau2Crystal.dmap / |-- aChateau2Crystal.gdml / |-- aChateau2Crystal_bare.amap / |-- aChateau2Crystal_bare.dmap / `— aChateau2Crystal_bare.gdml	DetectorFactory/Arrays/ / |-- AGATA_180.amap / |-- AGATA_180.dmap / |-- AGATA_180.gdml / |-- Builders / | |-- AGATA_180.dfb / | |-- Chateau2Crystal.dfb / | `-- EXOGAM.dfb / |-- Chateau2Crystal.amap / |-- Chateau2Crystal.dmap / `— Chateau2Crystal.gdml

Any of the listed detector could be seen/used in any of the STOGS/GEANT4 programs [see previous sections]. Since the informations regarding the detectors are saved in .gdml and two additional ascii files, the setup is also available in a ROOT session to help for data analysis.
Coming back to the example of a setup with a PARIS cluster, an EXOGAM clover and an AGATA Triple cluster, it has been saved in the MyStore factory, as can be seen in the following:
tree DetectorFactory/MyStore/
DetectorFactory/MyStore/
|-- Builders
|   `-- empty.dfb
|-- MySetup.amap
|-- MySetup.dmap
`-- MySetup.gdml

SToGS also provides a ROOT macro to see a geometry in the factory. To do this, here is the sequence of commands[8]:
[8] Make sure the ROOT package you are using has been compiled with the GDML module
root -l
root [0] .L DetectorFactory/BrowserFactory.C
root [1] ShowDetector("DetectorFactory/MyStore/MySetup”)

You should get the following picture:

Alternatively, to get a more complete interface to play with the geometry:
root [1] ShowInEve("DetectorFactory/MyStore/MySetup”)
The MySetup.gdml is used to draw the geometry [it contains the different volumes, shapes, materials, placements]. The MySetup.amap is:
PWLV|0	C 0 0 1 1	S /SToGS/SD/CopCluster	F -
PWLV|1	C 1 0 0 1	S /SToGS/SD/CopCluster	F -
ShapedCrystalA	C 0 0 1 1	S /SToGS/SD/CopCluster	F -
ShapedCrystalB	C 0 1 0 1	S /SToGS/SD/CopCluster	F -
ShapedCrystalC	C 1 0 0 1	S /SToGS/SD/CopCluster	F -
ShapedCrystalD	C 1 1 0 1	S /SToGS/SD/CopCluster	F -
BGORear	C 0 1 1 1	S /SToGS/SD/CopCluster	F -
CsIBack	C 1 0 1 1	S /SToGS/SD/CopCluster	F -
ARedCapsuleLV	C 0.6 0.6 0.6 0.75	S -	F -
ARedSpacingLV	C 1 1 1 0.5	S -	F -
ARedLV	C 1 0 0 1	S /SToGS/SD/Tracker	F -
BGreenCapsuleLV	C 0.6 0.6 0.6 0.75	S -	F -
BGreenSpacingLV	C 1 1 1 0.5	S -	F -
BGreenLV	C 0 1 0 1	S /SToGS/SD/Tracker	F -
CBlueCapsuleLV	C 0.6 0.6 0.6 0.75	S -	F -
CBlueSpacingLV	C 1 1 1 0.5	S -	F -
CBlueLV	C 0 0 1 1	S /SToGS/SD/Tracker	F -

- C is for the [RED:GREEN:BLUE:ALPHA] color [all values in range 0:1]
- S tells if the given volume is Sensitive or not [-] and the type of sensitivity. The AGATA array is a Tracker while other Arrays are calorimeters in the sense that what we have is the full energy deposited in the volume.
- F indicates the presence of a field (a possibility that is not used here).
MySetup.dmap summarizes how are organized the actives parts in terms of detector numbers, names [including history of construction] and positions. Note that, in the following example, the top parent volume of the PARIS phoswiches and EXOGAM clover constituents is the world, whereas the three AGATA crystals have an AGATA cluster as top parent volume, which explains the differences in numbering.
00000	CParisPW_2:000:ParisPW_2:000:PW:0:	0	CParisPW_2:000:ParisPW_2:000:PW:0:	0	+0 +0 +27.59  cm
00001	CParisPW_2:000:ParisPW_2:000:PW:1:	1	CParisPW_2:000:ParisPW_2:000:PW:1:	1	+0 +0 +37.75  cm
00002	CParisPW_2:000:ParisPW_2:001:PW:0:	2	CParisPW_2:000:ParisPW_2:001:PW:0:	2	+5.1801 +5.1801 +27.59  cm
00003	CParisPW_2:000:ParisPW_2:001:PW:1:	3	CParisPW_2:000:ParisPW_2:001:PW:1:	3	+5.1801 +5.1801 +37.75  cm
00004	CParisPW_2:000:ParisPW_2:002:PW:0:	4	CParisPW_2:000:ParisPW_2:002:PW:0:	4	+0 +5.1801 +27.59  cm
00005	CParisPW_2:000:ParisPW_2:002:PW:1:	5	CParisPW_2:000:ParisPW_2:002:PW:1:	5	+0 +5.1801 +37.75  cm
00006	CParisPW_2:000:ParisPW_2:003:PW:0:	6	CParisPW_2:000:ParisPW_2:003:PW:0:	6	-5.1801 +5.1801 +27.59  cm
00007	CParisPW_2:000:ParisPW_2:003:PW:1:	7	CParisPW_2:000:ParisPW_2:003:PW:1:	7	-5.1801 +5.1801 +37.75  cm
00008	CParisPW_2:000:ParisPW_2:004:PW:0:	8	CParisPW_2:000:ParisPW_2:004:PW:0:	8	-5.1801 +0 +27.59  cm
00009	CParisPW_2:000:ParisPW_2:004:PW:1:	9	CParisPW_2:000:ParisPW_2:004:PW:1:	9	-5.1801 +0 +37.75  cm
00010	CParisPW_2:000:ParisPW_2:005:PW:0:	10	CParisPW_2:000:ParisPW_2:005:PW:0:	10	-5.1801 -5.1801 +27.59  cm
00011	CParisPW_2:000:ParisPW_2:005:PW:1:	11	CParisPW_2:000:ParisPW_2:005:PW:1:	11	-5.1801 -5.1801 +37.75  cm
00012	CParisPW_2:000:ParisPW_2:006:PW:0:	12	CParisPW_2:000:ParisPW_2:006:PW:0:	12	+0 -5.1801 +27.59  cm
00013	CParisPW_2:000:ParisPW_2:006:PW:1:	13	CParisPW_2:000:ParisPW_2:006:PW:1:	13	+0 -5.1801 +37.75  cm
00014	CParisPW_2:000:ParisPW_2:007:PW:0:	14	CParisPW_2:000:ParisPW_2:007:PW:0:	14	+5.1801 -5.1801 +27.59  cm
00015	CParisPW_2:000:ParisPW_2:007:PW:1:	15	CParisPW_2:000:ParisPW_2:007:PW:1:	15	+5.1801 -5.1801 +37.75  cm
00016	CParisPW_2:000:ParisPW_2:008:PW:0:	16	CParisPW_2:000:ParisPW_2:008:PW:0:	16	+5.1801 +0 +27.59  cm
00017	CParisPW_2:000:ParisPW_2:008:PW:1:	17	CParisPW_2:000:ParisPW_2:008:PW:1:	17	+5.1801 +0 +37.75  cm
00018	EXOCLOVER_A-AC:000:CrystalA_P	18	EXOCLOVER_A-AC:000:CrystalA_P	18	+10.35 -2.61 -2.61  cm
00019	EXOCLOVER_A-AC:000:CrystalB_P	19	EXOCLOVER_A-AC:000:CrystalB_P	19	+10.35 -2.61 +2.61  cm
00020	EXOCLOVER_A-AC:000:CrystalC_P	20	EXOCLOVER_A-AC:000:CrystalC_P	20	+10.35 +2.61 +2.61  cm
00021	EXOCLOVER_A-AC:000:CrystalD_P	21	EXOCLOVER_A-AC:000:CrystalD_P	21	+10.35 +2.61 -2.61  cm
00022	EXOCLOVER_A-AC:000:BGO_P	22	EXOCLOVER_A-AC:000:BGO_P	22	+13.35 +0 +8.17425e-16  cm
00023	EXOCLOVER_A-AC:000:CsIBack_P	23	EXOCLOVER_A-AC:000:CsIBack_P	23	+23.35 +0 +1.42973e-15  cm
00024	ATC:000:AGATA-ARed:000:ARedCaps	24	ARed	0	-10.5903 -0.162832 +3.69279  cm
00025	ATC:000:AGATA-BGreen:000:BGreenCaps	24	BGreen	1	-10.5773 +3.2995 -1.18615  cm
00026	ATC:000:AGATA-CBlue:000:CBlueCaps	24	CBlue	2	-10.5833 -3.089 -1.52868  cm

- Column 1: unique number of the Sensitive Detector (SD) in this setup = number of the top parent volume + number of the SD inside its top parent.
- Column 2: unique name of the SD in this setup.
- Column 3: unique number of the parent volume of the SD (or number of the SD if its top parent is the world).
- Column 4: name of the SD inside its top parent (not unique if the parent is not the world).
- Column 5: number of the SD inside its top parent (not unique if the parent is not the world).
- Column 6: position of the SD.
## How to add detectors in the factories ?
To help adding more detectors in the factories, the SToGS_ImportGeo has been developped. It allows to import into gdml some geometries from other standard formats.
Here is snapshot of the program’s help (run the exe without any parameters)

To test SToGS_ImportGeo some standard, useful, geometry files, are provided within an extension of the SToGS package. To get them, inside the stogs directory, type :

git clone https://gitlab.in2p3.fr/IPNL_GAMMA/stogs_add-ons_geo add-ons_geo

It adds the add-ons_geo directory which includes sub-directories

add-ons_geo
├── Imports ... some fully imported geometries
├── README
├── dfb ... some examples of .dfb files
├── gdml ... pure gdml files produced by various converters
├── others ... pdf and various files defining geometries
├── ply ... .ply files, can be displayed with dedicated applications meshlab / FreeCAD etc ...
├── scripts ... useful script to help converting
├── step ... .step files from mechanical wrokshops and ...
├── stl ... .stl files, can be displayed with dedicated applications meshlab / FreeCAD etc ...
└── wrml ... .vrml files

Some .ply and .stl files are provided. For instance, the files ply/*ATC180.ply have been built using as input one of the ascii file (A180walls.list) of the initial AGATA Geant4 package. Such .ply have been also converted into .stl format using the meshlab application.
To convert one of them :
./geant4.10.XX-release/SToGS_ImportGeo -input add-ons_geo/ply/FrontWallATC180.ply -detname DetectorFactory/MyStore/FrontWallATC180

The default material is Aluminium, but this can be changed using

./geant4.10.XX-release/SToGS_ImportGeo ... -mat Pb ...

Note : the material should be known by SToGS or should be in the nist table provided by Geant4.

./geant4.10.XX-release/SToGS_ImportGeo ... -mat ACETONE ...
..
[W] in SToGS::MaterialConsultant::FindOrBuildMaterial ACETONE replaced by G4_ACETONE
..

Once you have produced the gdml equivalent in one of the SToGS factory, you can use the SToGS_DetectorBuilder to build your setup. Here for instance, the Aluminium walls are added to an ATC coming from Germanium factory (see add-ons_geo/dfb/ATCWithWall.dfb).
w DetectorFactory/Rooms/VR 1. 1. 1. m
+ DetectorFactory/SemiConductors/Ge/ATC 0. 0. 0. cm
+ DetectorFactory/Imports/ATC180SideWalls 0. 0. 0. cm
+ DetectorFactory/Imports/ATC180BackWall 0. 0. 0. cm
+ DetectorFactory/Imports/ATC180FrontWall 0. 0. 0. cm

On the left theATC as it is in the SemiConductor/Ge factory and on the right the same with the added walls which have been imported form .stl files

Another way to add more materials around detectors is to convert .step files, which can be provided by mechanical workshops, into .gdml files using other applications. For instance FastRAD can do this. There is also an online converter provided by psi. Once the conversion into done, they are two ways to use it in SToGS :

- just copy the gdml file (or files) in one factory and then you can use ‘as usual’
- or use the SToGS_ImportGeo exe to do the job
The difference is in the first case there are no .dmap/.amap files while they are produced using the second way. Such .amap/.damap files are not mandatory. If there are not there, all the information concerning the detector part relies on the .gdml file. So to change for instance a sensitivity or a color you have to do it directly in the .gdml while the .amap offers some quick ways. Gdml files produced from step using the psi converter are in the add_ons_geo director.

cp -r add-ons_geo/gdml/PARIS/GroupPMWithJunction2014 DetectorFactory/Imports/

allows to write then such .dfb file :

w DetectorFactory/Rooms/VR 1. 1. 1. m
+ DetectorFactory/Scintillators/SGParisPW_4 +00.000 +00.000 0. mm
+ DetectorFactory/Imports/GroupPMWithJunction2014/Top +00.000 +00.000 226.6 mm

which adds a PM tube to a PARIS phoswich.

./geant4.10.XX-release/SToGS_ImportGeo -input add-ons_geo/gdml/PARIS/GroupPMWithJunction2014/Top.gdml -detname DetectorFactory/MyStore/PPM2014

allows to write about the same .dfb file :

w DetectorFactory/Rooms/VR 1. 1. 1. m
+ DetectorFactory/Scintillators/SGParisPW_4 +00.000 +00.000 0. mm
+ DetectorFactory/MyStore/PPM2014 +00.000 +00.000 226.6 mm

which adds also a PM tube to a PARIS phoswich.
With this command

cp add-ons_geo/Imports/PARIS/* DetectorFactory/Imports/

and a .dfb file containing

w DetectorFactory/Rooms/VR 1. 1. 1. m
[
* DetectorFactory/Scintillators/SGParisPW_4 +00.000 +00.000 0. mm
* DetectorFactory/Scintillators/SGParisPW_4 +57.001 +57.001 0. mm
* DetectorFactory/Scintillators/SGParisPW_4 +00.000 +57.001 0. mm
* DetectorFactory/Scintillators/SGParisPW_4 -57.001 +57.001 0. mm
* DetectorFactory/Scintillators/SGParisPW_4 -57.001 +00.000 0. mm
* DetectorFactory/Scintillators/SGParisPW_4 -57.001 -57.001 0. mm
* DetectorFactory/Scintillators/SGParisPW_4 +00.000 -57.001 0. mm
* DetectorFactory/Scintillators/SGParisPW_4 +57.001 -57.001 0. mm
* DetectorFactory/Scintillators/SGParisPW_4 +57.001 +00.000 0. mm
]
+ DetectorFactory/Imports/PCMuShield2014 0 0 +52.2 mm
+ DetectorFactory/Imports/SC2014 0 0 +52.2 mm
+ DetectorFactory/Imports/PPM2014 +00.000 +00.000 226.6 mm
+ DetectorFactory/Imports/PPM2014 +57.001 +57.001 226.6 mm
+ DetectorFactory/Imports/PPM2014 +00.000 +57.001 226.6 mm
+ DetectorFactory/Imports/PPM2014 -57.001 +57.001 226.6 mm
+ DetectorFactory/Imports/PPM2014 -57.001 +00.000 226.6 mm
+ DetectorFactory/Imports/PPM2014 -57.001 -57.001 226.6 mm
+ DetectorFactory/Imports/PPM2014 +00.000 -57.001 226.6 mm
+ DetectorFactory/Imports/PPM2014 +57.001 -57.001 226.6 mm
+ DetectorFactory/Imports/PPM2014 +57.001 +00.000 226.6 mm
a full PARIS Cluster equiped with PM tubes, mu-metal and mechanical structure can be built.

A full PARIS Cluster in Geant4/Qt

To build a more complex setup it might be useful to go step by step: Build first a full PARIS cluster and save it using the command DetectorFactory/Save. Once saved in a factory the full cluster could be used to build such configuration :

See the add-ons_geo/dfb/ for more exemples.

## Some detectors availables in the different factories[9]
[9] Not exhaustive ! Do not hesitate to browser directly the factories to check what is available.

Scintillators
FATIMA
The basic modules [FATIMAM] have been implemented from the C++ code, work done by M.Labiche, available in the AGATA package. Because the shapes / placements are very simples, the detectors have been added to the Scintillator factory. It comes with two options (bare or not). A Quad is provided regrouping 4 modules and an array of four quad.
DetectorFactory/Scintillators/
├── FATIMAM.amap
├── FATIMAM.dmap
├── FATIMAM.gdml
├── FATIMAM_bare.amap
├── FATIMAM_bare.dmap
├── FATIMAM_bare.gdml
├── FATIMAQ.amap
├── FATIMAQ.dmap
├── FATIMAQ.gdml
├── FATIMAQ_bare.amap
├── FATIMAQ_bare.dmap
├── FATIMAQ_bare.gdml

Here are some snapshots :

PARIS

Different version of the PARIS Phoswich are provided. There are versions inherited from the PARIS Simulation package (DetectorFactory/Scintillators/ParisPW* & CParisPW), they have been produced the R&D phase of PARIS : they represents ideal version of phoswiches.

DetectorFactory/Scintillators/ / ├── ParisPW_2-bare.amap / ├── ParisPW_2-bare.dmap / ├── ParisPW_2-bare.gdml / ├── ParisPW_2.amap / ├── ParisPW_2.dmap / ├── ParisPW_2.gdml / ├── ParisPW_3-bare.amap / ├── ParisPW_3-bare.dmap / ├── ParisPW_3-bare.gdml / ├── ParisPW_3.amap / ├── ParisPW_3.dmap / ├── ParisPW_3.gdml / ├── CParisPW_2-bare.amap / ├── CParisPW_2-bare.dmap / ├── CParisPW_2-bare.gdml / ├── CParisPW_2.amap / ├── CParisPW_2.dmap / ├── CparisPW_2.gdml

Additionnal versions are available corresponding to more realistic geometries of the phoswiches obtained after the R&D phase of PARIS.
├── SCParisPW.amap / ├── SCParisPW.dmap / ├── SCParisPW.gdml / ├── SCParisPW_bare.amap / ├── SCParisPW_bare.dmap / ├── SCParisPW_bare.gdml / ├── SGParisPW_2-bare.amap / ├── SGParisPW_2-bare.dmap / ├── SGParisPW_2-bare.gdml / ├── SGParisPW_2.amap / ├── SGParisPW_2.dmap / ├── SGParisPW_2.gdml / ├── SGParisPW_3-bare.amap / ├── SGParisPW_3-bare.dmap / ├── SGParisPW_3-bare.gdml / ├── SGParisPW_3.amap / ├── SGParisPW_3.dmap / ├── SGParisPW_3.gdml / ├── SGParisPW_4-bare.amap / ├── SGParisPW_4-bare.dmap / ├── SGParisPW_4-bare.gdml / ├── SGParisPW_4.amap / ├── SGParisPW_4.dmap / ├── SGParisPW_4.gdml

One can see three versions of the Saint Gobain phoswiches (made of LaBr3) and, separated on the picture form the others, the SCIONIX phoswich made of CeBr3.

Chateau de Crystal
The basic shape of one module of the chateau de crystal is provided together with one configuration which could be used as an example how to build an array.

DetectorFactory/Scintillators/
├── aChateau2Crystal.amap
├── aChateau2Crystal.dmap
├── aChateau2Crystal.gdml
├── aChateau2Crystal_bare.amap
├── aChateau2Crystal_bare.dmap
└── aChateau2Crystal_bare.gdml

DetectorFactory/Arrays
├── Builders
│   ├── Chateau2Crystal.dfb
├── Chateau2Crystal.amap
├── Chateau2Crystal.dmap
├── Chateau2Crystal.gdml

EDEN
EDEN is a detector to detect neutrons. On left a decomposed shape of the detector

DetectorFactory/Scintillators/
├── EDEN_bare.amap
├── EDEN_bare.dmap
├── EDEN_bare.gdml
├── EDEN_v0.amap
├── EDEN_v0.dmap
├── EDEN_v0.gdml

SemiConductors
EUROBALL
Some of the EUROGAM-BALL detectors are included in the Ge factory. It includes phase 1 [so-called tapered], phase 2 [so-called clover] and phase 3 [so-called cluster]. For the tapered and clover three options are available allowing the construction from left to right of a bare detector which is composed of only active elements, a full detector including Al material and a detector with some collimators.

Clusters are not defined with that much details. There are known in the SToGS factory only tentatively since the exact cotes are not well known. As well, thoses detectors, event if the crystals are still there, they are not used anymore as such. As a consequence, a EUROBALLIII arrays is provided 'uncomplete' since in the geometry the clusters does not include Al dead layers as it is for the tapered and clovers.

DetectorFactory/Arrays
├── Builders
│   ├── EUROBALL_III.dfb
├── EUROBALL_III.amap
├── EUROBALL_III.dmap
├── EUROBALL_III.gdml

DetectorFactory/SemiConductors/
└── Ge
    ├── EURO-PI.amap
    ├── EURO-PI.dmap
    ├── EURO-PI.gdml
    ├── EURO-PII.amap
    ├── EURO-PII.dmap
    ├── EURO-PII.gdml
    ├── EURO-PIII.amap
    ├── EURO-PIII.dmap
    ├── EURO-PIII.gdml
    ├── EURO-PIII_colli.amap
    ├── EURO-PIII_colli.dmap
    ├── EURO-PIII_colli.gdml
    ├── EURO-PII_bare.amap
    ├── EURO-PII_bare.dmap
    ├── EURO-PII_bare.gdml
    ├── EURO-PII_colli.amap
    ├── EURO-PII_colli.dmap
    ├── EURO-PII_colli.gdml
    ├── EURO-PI_bare.amap
    ├── EURO-PI_bare.dmap
    ├── EURO-PI_bare.gdml
    ├── EURO-PI_colli.amap
    ├── EURO-PI_colli.dmap
    ├── EURO-PI_colli.gdml

EXOGAM

DetectorFactory/SemiConductors/Ge/
├── EXOCLOVER_A-AC.amap
├── EXOCLOVER_A-AC.dmap
├── EXOCLOVER_A-AC.gdml
├── EXOCLOVER_A-bare.amap
├── EXOCLOVER_A-bare.dmap
└── EXOCLOVER_A-bare.gdml

DetectorFactory/Arrays/
├── Builders
│   ├── EXOGAM.dfb
├── EXOGAM.amap
├── EXOGAM.dmap
├── EXOGAM.gdml

AGATA

DetectorFactory/Arrays/
├── AGATA_180.amap
├── AGATA_180.dmap
├── AGATA_180.gdml
├── Builders
│   ├── AGATA_180.dfb

DetectorFactory/SemiConductors/Ge/
├── AGATA-ARed.amap
├── AGATA-ARed.dmap
├── AGATA-ARed.gdml
├── AGATA-ARed_bare.amap
├── AGATA-ARed_bare.dmap
├── AGATA-ARed_bare.gdml
├── AGATA-BGreen.amap
├── AGATA-BGreen.dmap
├── AGATA-BGreen.gdml
├── AGATA-BGreen_bare.amap
├── AGATA-BGreen_bare.dmap
├── AGATA-BGreen_bare.gdml
├── AGATA-CBlue.amap
├── AGATA-CBlue.dmap
├── AGATA-CBlue.gdml
├── AGATA-CBlue_bare.amap
├── AGATA-CBlue_bare.dmap
├── AGATA-CBlue_bare.gdml
├── ATC.amap
├── ATC.dmap
├── ATC.gdml
├── ATC_bare.amap
├── ATC_bare.dmap
├── ATC_bare.gdml
├── Builders
│   ├── agata_capsule.geo
│   ├── agata_cluster.geo
│   ├── agata_cluster_ori.geo
│   ├── agata_euler.geo

PlainDetectors
This factory produces GEANT4 basics shapes [cube, sphere, tube]. Such plain detectors could be used for tests. The .gdml, .dmap or .amap files could be modified directly depending of your needs. The detector can also be copied first in your Store (DetectorFactory/MyStore) so that you can operate on copies without altering the one produced by SToGS. A ROOT function helps you to copy a detector form a factory to another:
root [0] .L DetectorFactory/BrowserFactory.C
root [1] RenameSToGSDetector("DetectorFactory/PlaneDetectors/PLANE_tube","DetectorFactory/MyStore/MyTube")

Generics
This factory contains some detectors that are built using a configuration file. It is the case for the detector called TwoShells. For such detectors, there are no .gdml, .amap and .dmap files created. As for any setup/detectors, the user can however save such detector in his own factory [MyStore].
To add such a detector, in the .dfb file, just add the following line:
+ DetectorFactory/Generics/TwoShells$MyTwoShells.geo 0. 0. 0. m
after having customized the configuration file MyTwoShells.geo which is expected in the directory DetectorFactory/Generics. There is an example of such a file in the sub-directory Demos.

Imports
This factory contains some detectors that have been imported into SToGS, from other frameworks, through GDML. If you want to delete such files, you should be very careful since the way they have been produced is not included in the SToGS package. The following pages give an overview of some imported geometries together with some informations concerning their origins.

Silicone detector from Koeln
Origin : AGATA GEANT4 code.
Problems found :

Silicone ring, with passive layers, provided together with a mask [absorber] of the same dimensions.

DetectorFactory/Imports/
├── KoelnSi.amap
├── KoelnSi.dmap
├── KoelnSi.gdml
├── KoelnSiABSORBER.amap
├── KoelnSiABSORBER.dmap
├── KoelnSiABSORBER.gdml

Recoil Filter Detector

Origin : AGATA GEANT4 code.
Problems found :

Mylar foils are the active part of the RFD. The factory provides alsa some add ons as shown of the right picture.

DetectorFactory/Imports/
├── RFD_addons.amap
├── RFD_addons.dmap
├── RFD_addons.gdml
├── RFD_bare.amap
├── RFD_bare.dmap
└── RFD_bare.gdml

NeutronWall

Origin : AGATA GEANT4 code. Credit for the geometry Joa Ljungval

Problems found :
G4Trap used with the constructor (Name,Vertices) is not exported in GDML correctly
→ Pb of orientation … i.e. Definition of the right direction with such a constructor ?
→ Switch to G4GenericTrap
- The Vacuum material gives problems also because in the GDML file an element with a similar name exists [bugs ?? Solved or to be solved ??]. To get rid of it, in the gdml, the element has been renamed [by adding _el].
- The NW is composed of two types of Hexagones. The use of G4GenericTrap adds a tiny overlapping which has been removed by reducing the housing external walls by 0.5mm.
- Two versions of the NW have been imported in SToGS. The bare one [right part of the picture] is the same as the full one [left part] with the Aluminium parts replaced by some air (except the vacuum part filling the end of the housing).

The two detectors are in DetectorFactory/Imports as A_NWALL and A_NWALL_bare :

DetectorFactory/Imports/
├── A_NWALL.amap
├── A_NWALL.dmap
├── A_NWALL.gdml
├── A_NWALL_bare.amap
├── A_NWALL_bare.dmap
└── A_NWALL_bare.gdml

DIAMANT

Origin : AGATA GEANT4 code. Credit for the geometry G. Jaworski

Problems found :
G4Tet used is not exported in GDML so far [02/2015]
→ Such shapes are used for Triangles in corners
→ Switch to G4GenericTrap
Problems of identical names used for 'different' shapes [i.e. classe instance]
→ Switch to unique names
The Tantalum material gives problems because in the GDML file an element with a similar name exists [GDML bugs ?? Solved or to be solved ??]. To get rid of it, in the gdml, the element has been renamed [by adding _el].

The detectors are in DetectorFactory/Imports as
A_DIAMANT and A_DIAMANT_bare
A_DIAMANT_Back and A_DIAMANT_Back_bare
A_DIAMANT_Forw and A_DIAMANT_Forw_bare
A_DIAMANT_FForw and A_DIAMANT_FForw_bare
A_DIAMANT_Ring and A_DIAMANT_Ring_bare
A_DIAMANT_Wall and A_DIAMANT_Wall_bare

# Action Manager
As explained in the section “Running a SToGS application”, once the setup is established using the SToGS_DetectorBuilder, the simulation itself could be run and it is important then for the user to extract from GEANT4 useful informations. To do that, GEANT4 provides hooks that are called at different levels/steps during the simulation process. In SToGS, all those possibilities are managed by the Action Manager. Several sets of actions are proposed in the package and the user also has the possibility to write his own one. Here is a part of the input file [SToGS_Source.conf] used to configure the SToGS_Source application, where several action managers can be seen:
...
# The UserActionInitialization (which deals without outputs and the generator [thread local objects])
#
#actions: printout run;event;track;
#actions: ascii setup/SToGS_ascii_actions.conf
actions: outtree setup/SToGS_tree_actions.conf
#actions: stogstree setup/SToGS_tree_actions.conf
#
...

The first action manager, called printout, just displays on the terminal what is going on at different steps of the simulation process, depending on the string provided. With the string given previously (run;event;track;), something is written at the beginning/end of run/event/track.
G4WT3 > Begin of Event: 1
G4WT3 > Begin of Track: (PreUserTrackingAction)
G4WT3 > PARTICLE: gamma
G4WT3 > TRACK ID: 2
G4WT3 > PARENT ID: 0
G4WT3 > TOTAL ENERGY: 200 keV
G4WT3 > KINETIC ENERGY: 200 keV
G4WT3 > VELOCITY: 299.792
G4WT3 > VOLUME WHERE THE PARTICLE WAS KILLED: Cblue
G4WT3 > End of Track: (PostUserTrackingAction)
G4WT3 > Begin of Track: (PreUserTrackingAction)
G4WT3 > PARTICLE: e-
G4WT3 > TRACK ID: 4
G4WT3 > PARENT ID: 2
G4WT3 > TOTAL ENERGY: 639.906 keV
G4WT3 > KINETIC ENERGY: 128.907 keV
G4WT3 > VELOCITY: 180.452
G4WT3 > VOLUME WHERE THE PARTICLE WAS KILLED: Cblue
G4WT3 > End of Track: (PostUserTrackingAction)
G4WT3 > Begin of Track: (PreUserTrackingAction)
G4WT3 > PARTICLE: e-
G4WT3 > TRACK ID: 3
G4WT3 > PARENT ID: 2
G4WT3 > TOTAL ENERGY: 571.025 keV
G4WT3 > KINETIC ENERGY: 60.0258 keV
G4WT3 > VELOCITY: 133.795
G4WT3 > VOLUME WHERE THE PARTICLE WAS KILLED: Cblue
G4WT3 > End of Track: (PostUserTrackingAction)
G4WT3 > Begin of Track: (PreUserTrackingAction)
G4WT3 > PARTICLE: gamma
G4WT3 > TRACK ID: 1
G4WT3 > PARENT ID: 0
G4WT3 > TOTAL ENERGY: 100 keV
G4WT3 > KINETIC ENERGY: 100 keV
G4WT3 > VELOCITY: 299.792
G4WT3 > VOLUME WHERE THE PARTICLE WAS KILLED: Cblue
G4WT3 > End of Track: (PostUserTrackingAction)
G4WT3 > Begin of Track: (PreUserTrackingAction)
G4WT3 > PARTICLE: e-
G4WT3 > TRACK ID: 5
G4WT3 > PARENT ID: 1
G4WT3 > TOTAL ENERGY: 599.932 keV
G4WT3 > KINETIC ENERGY: 88.933 keV
G4WT3 > VELOCITY: 157.064
G4WT3 > VOLUME WHERE THE PARTICLE WAS KILLED: Cblue
G4WT3 > End of Track: (PostUserTrackingAction)
G4WT3 > End of Event: 1

The second one, ascii, would save what is going on in the sensitive part of the array in an ascii file. The format (almost identical to the one of the AGATA package) is given in the following picture (left panel). While the first one is convenient for debugging, this second one is more adapted to fast developments: ascii files are readable for humans but not effcient since it requires large amount of disk to store the infomation.
# FORMAT: 'C' ID1 ID2 Energy(keV) x(cm) y(cm) z(cm) / # with X=P for primary gammas and in this case: / # ID1 is the vertexID, ID2 the total number of primaries / # E the energy of the emitted gamma / # x,y,z represents the momentum / # with X=H for a single hit and in this case: / # ID1 is the vertexID it comes from, ID2 the detector number / # E the energy of the impact / # x,y,z represents its position / # / P 1 1 661.789 0.186708 -0.208238 0.599784 / H 1 0 38.925 1.89502 -3.06451 13.8729 0.521311 / H 1 0 112.016 1.8957 -3.06448 13.8732 0.521353 / H 1 0 69.9853 2.04822 -3.1023 13.2777 0.500799 / H 1 0 250.522 1.56354 -3.05809 13.1898 0.484457 / H 1 0 190.34 3.04463 -3.39513 9.77698 0.3599 / P 1 1 661.659 -0.263225 -0.0943591 0.599668 / H 1 0 38.925 -9.74733 1.43029 1.91934 0.980162 / H 1 0 37.6982 -9.74744 1.4303 1.9193 0.980173 / H 1 0 48.5859 -1.37445 -2.73302 9.54417 0.349731 / H 1 0 43.764 -1.37471 -2.73193 9.5412 0.349834 / H 1 0 33.1879 -1.37737 -2.72824 9.54207 0.349948 / H 1 0 31.9853 -1.37407 -2.7275 9.5435 0.350039 / H 1 0 202.16 -1.37345 -2.72591 9.54428 0.350129

This is why a third one, outtree, has been developed into SToGS. Obviously, as for EGPS, it requires to have ROOT installed on the computer. It follows also the same approach by giving the user the possibility to configure what is to be saved. Here is a typical content of the configuration file SToGS_tree_actions.conf.

# Directory where to store the produced files
#
path: /path/to/the/output/data
#
# Base Name used for the ROOT files
#
basename: MyROOT
#
# Print Message on the terminal every modulo recorded events
#
modulo: 1000000
#
# MAX # of events per files
#
#max_size: 50000
#
# auto save option
#
#auto_save: -500000000
#
# RECORD options 0 means all, 1 only events that have deposited at least one hit in the full array
#
record_option: 0
#
#
# Tree Name and Title. Title is used to determined what to be stored in the ROOT file
#
tree: MyTreeFromSToGS Pr.E;Pr.PDG;Ev.E;Ev.X;Ev.Y;Ev.Z;Ev.H

As it can be seen on the last line, where the name (MyTreeFromSToGS) of the TTree is given, another string is provide (also used as title of the tree) which tells the system what information should be written in the output TTree: in this case, information regarding the primary events [Pr] (energy, type of the particle) and information concerning the hits [Ev.] in the full setup (energy Ev.E, position Ev.XYZ for one hit, full energy deposited in the array Ev.H).

An additional Action Manager stogstree is provided into STOGS. It allows to store a lot of information on the primary event and on the collected event: it is less flexible that outstree which is the one recommended to be used. However, since it is the first facility provided into SToGS, information on how to use it is kept there. It required to pre-compile a library which is provided into the analysis/stogs sub-directory. Go there and do make:

cd analysis/SToGS
make.

This should provide the library libSToGS_BaseROOTEvents.so. Once done, you should re-configure SToGS and re-compile it: you should see such lines:
[SToGS] ROOT has been found: somepath/to/lib
--> Cool, libSToGS_BaseROOTEvents.so found in analysis !
[SToGS] SToGS Compiled with ROOT facilities

The configuration file is identical to the outtree’s one except the tree title is ignored and it is not possible to configure what branch is to be kept. Here is a snaphot showing such the obtained tree structure.

Different examples of configuration files could be found in the setup/SToGSDefault sub-directory.