## Slide 1
A novel facility for ERL development and applications in multi-turn configuration and high-power regime
Venice, May 10th 2023
Walid KAABI on behalf of PERLE Collaboration

## Slide 2: Introduction- ERL Concept
Injector
Beam dump
Superconducting Linac
ERL Loop
acceleration
deceleration
Acceleration to the top energy
Beam used in IP
Kinetic energy of used beam recycled to re-excite cavities
New beam injected in ERL loop
More advantages:
Linac-like beam quality with extremely flexible time structure
High operating efficiency
Multi-pass configuration: High average current carrying capability (no more RF power limit) + High average beam power in a compact machine
The benefits:
Reduce accelerator power consumption
Dumping the beam at injection power
Fresh beam in IP with the same characteristics
Acceleration:
RF power provided to cavities
The idea:
(1)
(2)
(3)
(4)
(1’)
ERL Loop
(2’)…
Deceleration:
180° RF Phase shift

## Slide 3: ERL - The global landscape
Technology Limited
Funding Limited

## Slide 4: ERLs in the European Accelerator R&D Roadmap
ERL development has been recognized as one of the five main axis of accelerators R&D in support of the European Strategy for Particle Physics (ESPP):
  High-field magnets
  High-gradient RF structures and systems
  High-gradient plasma and laser accelerators
  Bright muon beams and muon colliders
  Energy Recovery Linacs
The ERL Roadmap Panel, chaired by Max Klein and Andrew Hutton, has done a tremendous job with broad and active participation. PERLE & bERLinPro projects were recognized as one of the "essential pillars of the ERL development," with milestones to be achieved by the next ESPP in 2026.
ESPP R&D Accelerator Roadmap: https://arxiv.org/ftp/arxiv/papers/2201/2201.07895.pdf

## Slide 5: The short story of the PERLE Genesis
Future particle physics imposes strong challenges on accelerators and requires a variety of accelerator R&D programs not only to meet the foreseen performances, but also to lower their energetic consumption and enhance their efficiency.
   Energy Recovery Linacs offer one of the main options for energy frontier colliders
To probe deep inelastic scattering at high energy and to study the Higgs boson, LHeC proposes a high luminosity collider using the HL-LHC protons and an intense electron beam.
For the electron beam, the ERL scenario has many advantages :
  High luminosity, low interference for installation next to LHC, machine size, energy consumption
  Concept also applied to the FCC-eh design
The ERL-ring collider concept of LHeC based on
  synchronous operation of HL-LHC and 50 GeV electron beams
  circumference of e- loop about 1/5 of that of LHC (5.3 km)
  luminosity of 1034 cm-2.s-1
  Multi-turn ERL (3+3 passes), 50 GeV, RF frequency: 801 MHz,
  20 mA beam current (6 x 20 = 120mA load in the cavities).

## Slide 6: PERLE Configuration
PERLE: first multi-turn ERL, based on SRF technology, designed to operate at 10MW (20 mA, 500 MeV) power regime
 A hub to explore a broad range of accelerator phenomena and to validate technical choices improving accelerators efficiency in an unexplored operational power regime on the pathway of the ERL technology development for future energy and intensity frontier machines.
350-500 kV
DC gun
HV tank
Booster: 5 single-cell cavities (802MHz) individually powered
Buncher
Merger
Light box
Green laser 40 MHz
Photocathodes loading chamber (Sb-based photocathodes)
Cryomodule with 4 five-Cell cavities
Total gradient 82 MeV
3 acc & 3 decc beams at different energies travelling in the CM.
Injection line delivering 500pC bunches at 7 MeV.
3 staked isochronous recirculation arcs for beams at different energies (Arcs 1, 3, 5).
Interaction Points
Switchyard: vertical separation/recombination of beams at different energies
3 staked (& inversed) isochronous recirculation arcs for beams at different energies (Arcs 2, 4, 6)
Target Parameter | Unit | Value
Injection energy | MeV | 7
Electron beam energy | MeV | 500
Normalised Emittance γεx,y | mm mrad | 6
Average beam current | mA | 20
Bunch charge | pC | 500
Bunch length | mm | 3
Bunch spacing | ns | 25
RF frequency | MHz | 801.58
Duty factor |  | CW
Beam dump

## Slide 7: PERLE Timeline for TDR phase and beyond
Phase 3: PERLE 500 MeV version
Technical Design phase (TDR)
Installation phases
Phase 1: Installation of the injection line
Phase 2: PERLE 250 MeV version
2020
2021
2022
2023
2024
2025
2026
2027
2028
2029
2031
2030
Prepare to Build phase (P2B)

## Slide 8: PERLE Lattice optimization
Lattices and optics for the 500 MeV and 250MeV PERLE versions were studied and optimised:
A full 1st order calculation were finished and a complete 250 and 500 MeV lattice is now available.
The stability of the lattice was crosscheck with different codes (OPTIM6, MADX & BMAD).
First specifications of quadrupoles and dipoles in switchyards & arc sections are obtained.
 Further studies are ongoing/to be done: momentum acceptance, correction of nonlinear aberrations with multipoles, longitudinal match…
 In addition to beam dynamics studies: Start to end simulations with CSR and microbunching, Multiparticle tracking, BBU, Impedance analysis and Wakefield effect mitigation …

## Slide 9: Lattice optimization of the 500 MeV version of PERLE
BETA_X
BETA_Y
DISP_X
DISP_Y
Arc 1
20.94
0
40
0
1
-1
BETA_X&Y[m]
DISP_X&Y[m]
S = 56 × lRF
20.94
0
40
0
1
-1
BETA_X&Y[m]
DISP_X&Y[m]
Arc 3
S = 56 × lRF
254 MeV
89 MeV
20.94
0
40
0
1
-1
BETA_X&Y[m]
DISP_X&Y[m]
Arc 5
S = 56 × lRF
418 MeV
IR
Arc 2
S = 57 × lRF
21.32
0
30
0
1
-1
BETA_X&Y[m]
DISP_X&Y[m]
171 MeV
Arc 4
S = 57 × lRF
336 MeV
21.32
0
30
0
1
-1
BETA_X&Y[m]
DISP_X&Y[m]
Arc 6
S = 60½ × lRF
IR
500 MeV
22.63
0
30
0
1
-1
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
S.A. Bogacz et al. International Workshop on Deep-Inelastic Scattering and Related Subjects- Stony Brook University, New York, USA (2021), doi:10.21468/SciPostPhysProc.

## Slide 10: Lattice optimization of the 250 MeV version of PERLE
Transverse beam size (3( and Low beta function @ the 2 IRs
Alexis Fomin et al. “Lattice design of 250 MeV version of PERLE”- IPAC’23- TUPL171

## Slide 11: Bunch Filling Pattern studies
In the injection line:
500 pC e- bunchs generated at finj= 40 MHz
  time spacing between bunches: 25 ns
  average current: 20 mA
Bunches accelerated to 7 MeV in the injector then injected into the ERL loop
ERL Loop:
Cavity frequency: fRF= 801,58 MHz (lRF= 34.7 cm)
fRF/finj = 20
Length spacing between bunches: 20 lRF
During the 1st Pass:
Linac 1  Arc 1  Linac 2  Arc2
7  89 MeV 89  171 MeV
1st Pass length= 167 lRF
8 bunchs injected in the 1st pass.
The 9th bunch Injected is followed by the 1st accelerated bunch in pass 1 that start pass 2 (spaced by 7 lRF).
Pass 1
Pass 1-2
Pass 1-6

## Slide 12: Bunch Filling Pattern 250 MeV Vs. 500 MeV version

## Slide 13: Injection line optimisation
A conceptual design of the PERLE injector was made within a collaboration between AsTeC-Daresbury, UoL and IJCLab. This included the DC gun cathode shape optimisation, a buncher cavity and the merger conceptual designs, besides a complete beam dynamic studies of space charge effects, phase space and bunch distributions, and emittance. Further studies and design optimisation of the injector are currently undertaken.
Transverse phase space (x-px)
Longitudinal phase space (z-pz)
Solenoids focus beam in transverse plans
Buncher focus beam in longitudinal
M shape in z-pz axis at the end of injector : Might be a problem
350 kV
DC gun
HV tank
Booster: 5 single-cell cavities (802MHz) individually powered
Buncher
Merger
Light box
Green laser 40 MHz
Photocathodes loading chamber (Sb-based photocathodes)
B. Hounsell et al. “Conceptual design of the PERLE injector” LINAC’22- Liverpool, UK- THPOJO26

## Slide 14: PERLE SRF cavity
PERLE Requirements | Impacts | Challenges | Possible Solutions
CW operation (RF) | High dynamic losses | The highest cavity Q0 | Cavity post-treatment (Doping, infusion…)
High current operation | High HOMs excitation | Efficient HOMs extraction & damping | Act on cavity design: low frequency cavity choice (< 1GHz), larger cavity aperture, fewer cells for the a given gradient, optimisation of end-cell design.
Muti-bunches operation | Increase beam instabilities | The highest BBU threshold | Regular spacing of bunches: optimisation of the bunch filling pattern during Lattice design + BBU study after HOM optimisation (including collective effects).
First Nb 802 MHz 5-Cell cavity fabricated @ JLAB
PERLE requirements
Q0 (2k) = 3 e10 @ ~27 MV/m
Quench @ Eacc ~ 30 MV/m
A 5-Cell copper cavity is under fabrication @Jlab to allow end group design optimisation and to test several HOM couplers combinations to assess the best HOM damping scheme.
F. Marhauser et al. “802 MHz ERL cavity design and development”- IPAC2018 (Vancouver, BC, Canada)- doi:10.18429/JACoW-IPAC2018-THPAL146

## Slide 15: Status of HOM design studies:
HOM coupler optimization of 3 different designs
Couplers were geometrically optimized according to HOM spectrum (and ) & S-parameters btw port 1 (beam pipe) & port 2 (coupler output) were studied.
The hook coupler provides higher damping of the first two dipole passbands (TE111 and TM110)
The DQW coupler exhibits a better monopole coupling for TM010 mode than the probe design.
Study of 2 damping schemes with 4 HOM couplers (Especially for dipole HOM extraction)
 Promising results of the 4 DQW scheme: It allows damping both monopole and dipole HOMs below the analytically-computed beam-stability limits
Monopole transmission
TM010
TM011
TM012
Optimized region
TE111
TM110
TM111
Dipole transmission
Optimized region
Longitudinal impedance spectra of the cavity
Transverse impedance spectra of the cavity
beam
beam
beam
Probe Coupler
DQW Coupler
Hook Coupler

## Slide 16: Status of HOM studies :
Installation in a double-cell Cu cavity and test of performances (S12, QL and Qext) @JLab
3D-printed prototype (Epoxy Accura 48) copper-coated @CERN
From RF design to performance measurements: Example of a fruitful collaborative effort between IJCLab, Jefferson Lab & CERN
Measurements are made as a function of rotation angle of HOM coupler hook.
Good rejection of Fundamental Mode, Qext > 1E+09.
Measured Qext for HOMs are below BBU limit thresholds.
Good agreement between measured and simulated Qext  could be improved with more appropriate boundary conditions at beam pipe apertures.
Hook coupler
Probe coupler
DQW coupler
C. Barbagallo et al. “First RF measurements of coaxial HOM coupler prototypes in a copper cavity for the PERLE project”- IPAC’23- MOPA025

## Slide 17: Cryomodule design:
Intermediate supporting structure (spaceframe)
Cavity string hung by rods
Insertion of the cavity string by the extremity (rollers)
Trap doors for tuner access
Connexion to the valve box on the top of the vacuum vessel
Important space available inside
Design validated: series fab. & tests ongoing (Qty 30)
ESS Cryomodule design was selected:
1st Cryomodule: Foreseen for 2027
Adapted from ESS design, it will be optimised for efficient high current ERL operation within the European Infra-Tech program iSAS*. It will host cavities equipped with HOM couplers and FPC optimised and developed within the same program.
2nd Cryomodule: Foreseen for 2030
May include some/all the technologies studied within iSAS program to improve the efficiency of Cryomodules: Fast Reactive Tuner (FRT) for microphonics mitigation, LLRF managed by AI and 4.2 K Cavities operating.
* More information on iSAS program: https://indico.ijclab.in2p3.fr/event/9521/

## Slide 18: PERLE e- Source
Installation of the former Alice DC Photogun (Daresbury) @ IJCLab-Orsay (January 2023)
Vacuum pumping of gun new chamber after ultrasonic cleaning (December 2022)
Installation of Daresbury DC gun
New opportunity under discussion
Ongoing discussions with Research Instruments GmbH (RI) to acquire a state-of-the-art e- photogun:
the DC gun is fabricated, commissioned and approved for high current operation.
C. Quitmann et al. «Test of a DC- Photogun injector for The Lighthouse Facility” – Proceedings for IPAC’23- TUPA020

## Slide 19
Conclusions
ERL machines open a new frontier for the physics of “the electromagnetic probe” (ep, eA, eN). PERLE is a key ERL project for HEP and Nuclear Physics communities
PERLE has been recognised (together with bERLinPro) an essential pillars of the ERL ESPP strategy. It will be the first ERL that combines high current and multi-passes (high luminosity/higher energy), designed to operate at 10 MW power regime.
PERLE is a very challenging machine : Though to be a hub to explore a broad range of accelerator phenomena and to validate technical choices improving accelerators efficiency in an unexplored operational power regime on the pathway of the ERL technology development for future energy and intensity frontier machines.
The International collaboration is formed and still opened to new comers.
Important boost in the last year in France and we are actively entered in the TDR and the P2B phases. The installation of the first brick of the machine (e- DC-gun) is ongoing.

## Slide 20
Sébastien Bousson
1972-2022
In the memory of Sébastien
Sébastien was an internationally recognized expert, who has worked throughout his career to lead R&D on superconducting accelerating systems. For more than twenty years, he put his skills and dynamism at the service of the discipline and assumed high responsibilities at IPNo, IJCLab and IN2P3-CNRS: project manager then manager of the SUPRATech technological platform, coordination of major work packages in large European programs (EURISOL, TIARA) or project manager of CNRS contribution to the European Spallation Source- ESS.
He was distinguished by the CNRS in 2015 with a crystal medal. With a real vision for the theme, he was one of the international experts involved in the European accelerator R&D strategy for the future of particle physics.
Since 2020, he has been Director of the Accelerator Physics pole and Associate Scientific Director of the IJCLab. Beyond his skills and his leadership, Sébastien is recognized for his great human qualities. His passing is a huge loss for the accelerator community, which pays him unanimous tribute.

## Slide 21
Acknowledgments
To all the colleagues that provides me with materials and contribute to the efforts presented:
Racha Abukechek, Hadil Abualrob, Kevin Andre, Robert Apsimon, Carmelo Barbagallo, Maud Baylac, Alex Bogacz, Sylvain Brault, Patricia Duchesne, Alex Fomin, Alexandre Gallas, Coline Guyot, Benjamin Hounsell, Gregory Iaquaniello, Max Klein, Etienne Labussiere, Rodolphe Marie, Julien Michaud, Boris Militsyn, Guillaume Olry, Gilles Olivier, Luc Perrot, Denis Reynet, Raphael Roux, Achille Stocchi, Peter Williams and Haipeng Wang.
PERLE related IPAC’23 contributions
Rasha Abukeshek et al. “Magnetic design of the commutational magnet and quadrupoles for PERLE accelerator”- MOPA023
Carmello Barbagallo et al. “First RF measurements of coaxial HOM coupler prototypes in a copper cavity for the PERLE project”- MOPA025
Alexis Fomin et al. “Lattice design of 250 MeV version of PERLE”- TUPL171
Coline Guyot et al. “Standing wave RF cavities modeling for multi-pass Energy Recovery Linac traking purpose”- TUPL170
Thank you for your attention!